## Slide 1
2. Mars Orbital Insertion / Parking Orbit
EEV Arrival Date: Jun 22, 2040
DST Arrival Date: Jun 27, 2040
Delta-V: 0.90 km/s
Parking Orbit Parameters:
Period: 5.0 days
Eccentricity: 0.84
SMA: 59000 km
4. Return to DST
Return Date: Jul 12, 2040
Transfer Time: 11 hrs.
Delta-V: 0.90 km/s
6. Return to DST
Return Date: Jul 26, 2040
Transfer Time: 4 days
Delta-V: 0.63 km/s
1. EEV Transfer Arc to Mars
Launch Date: Oct 9, 2039
Transfer Time: 256 days
Delta-V: 4.13 km/s
3. Transfer to Phobos
Transfer Date: Jul 2, 2040
Time on Phobos: 9.2 days
Delta-V: 0.83 km/s
5. Transfer to Deimos
Transfer Date: Jul 15, 2040
Time on Deimos: 4.9 days
Delta-V: 0.59 km/s

## Slide 2
Mission Logistics Optimization
Objective: Find Trajectory that minimizes the cost function:
- Rocket Eqn. used to convert ΔV to mass.
- Four sample trajectories (not entire solution space) below
- Trajectory #4 was selected for this mission
– Required propellant capacity of the EEV
– Required propellant from the DST
– Science time on Phobos (days)
– Science time on Deimos (days)
3. Deimos to Phobos, no stop at DST. = 16,898
ΔV = 2.41 km/s
= 10,103 kg
= 0 kg
= 11.32 days
= 7.56 days
4. Deimos to Phobos, refuel at DST. = 11,897
ΔV = 1.80 km/s
= 6,727 kg
= 3,793 kg
= 9.25 days
= 3.63 days
1. Phobos to Deimos, no stop at DST. = 15,868
ΔV = 2.20 km/s
= 8,854 kg
= 0 kg
= 10.52 days
= 9.35 days
2. Phobos to Deimos, refuel at DST. = 11,873
ΔV = 1.74 km/s
= 6,419 kg
= 2851 kg
= 9.24 days
= 4.91 days
1. Transfer Arc to Mars
Launch Date: Oct 9, 2039
Transfer Time: 256 Days
ΔV: 4.13 km/s
2. Parking Orbit Insertion
EEV Arrival Date: Jun 22, 2040
DST Arrival Date: Jun 27, 2040
ΔV: 0.90 km/s
Parking Orbit Parameters
Period: 5.0 days
Eccentricity: 0.84
SMA: 59000 km
3. Transfer to Phobos
Transfer Date: Jul 2, 2040
Time on Phobos: 9.2 days
ΔV: 0.83 km/s
4. Return to DST
Transfer Date: Jul 12, 2040
Transfer Time: 11 hours
ΔV: 0.90 km/s
5. Transfer to Deimos
Transfer Date: Jul 15, 2040
Time on Deimos: 4.9 days
ΔV: 0.59 km/s
6. Return to DST
Transfer Date: Jul 26, 2040
Transfer Time: 4 days
ΔV: 0.63 km/s

## Slide 3: Concept of Operations